Gosford Passing Loops Monitoring Data

| Licensee: | Downer Edi Works Pty Ltd | Address: | 15 Watt St, Gosford | EPL No. | 20269 |
| --- | --- | --- | --- | --- | --- |
| Sampled: | Throughout October | Obtained: | Throughout October | Published: | /2014 |

|  | Noise Monitoring Results |
| --- | --- |
| Location | Date | Time | Measured (LAeq 15 min) | Predicted noise level | Comments |
| 77 Showground Road | 07/10/14 | 2316 | 51.41 | 57.6 | Rail adjustment work. Measurement dominated by vehicles passing. |
| 77 Showground Road | 08/10/14 | 2123 | 56.7 | 57.6 | Rail adjustment work. Measurement dominated by vehicles passing, and freight train. |
| 77 Showground Road | 09/10/14 | 2246 | 50.2 | 57.6 | Rail adjustment work. Measurement dominated by vehicles passing. |
| Lindsay Street | 18/10/14 | 2200 | 59.2 | 74.0 | Recon work at 201 and 202 points. Rail adjustment work. Measurement dominated by construction vehicles passing and freight and passenger trains. |
| 31 Dwyer Street | 18/10/14 | 2225 | 50.7 | 65.8 | Recon work at 201 and 202 points. Rail adjustment work. Measurement dominated by construction vehicles passing. |
| 31 Dwyer Street | 18/10/14 | 1302 | 56.7 | 65.8 | Recon work at 201 and 202 points. Rail adjustment work. Measurement dominated by construction vehicles passing. |
| Lindsay Street | 18/10/14 | 1325 | 64.5 | 74.0 | Recon work at 201 and 202 points. Rail adjustment work. Measurement dominated by construction vehicles passing and freight and passenger trains. |
| Lindsay Street | 19/10/14 | 0803 | 53.6 | 74.0 | Recon work at 201 and 202 points. Rail adjustment work. Measurement dominated by construction vehicles passing and Sydney Trains works. |
| 31 Dwyer Street | 19/10/14 | 0940 | 56.7 | 65.8 | Recon work at 201 and 202 points. Rail adjustment work. Measurement dominated by construction vehicles passing and passenger train. |
| 24 Campbell Street | 28/10/14 | 1950 | 58.1 | 62.5 | Vacuum truck, excavation and dump truck being operated. Measurements dominated by vehicles passing, dog barking, and a train passing. |
| 24 Campbell Street | 28/10/14 | 2225 | 55.2 | 62.5 | Vacuum truck, excavation and dump truck being operated. Measurements dominated by vehicles passing, dog barking, and a passenger and freight train passing. |
| 24 Campbell Street | 29/10/14 | 1935 | 53.8 | 62.5 | Excavation and dump truck loading on Showground Road. Measurement dominated by vehicles passing, birds and dogs. |
| 24 Campbell Street | 29/10/14 | 2220 | 49.9 | 62.5 | Excavation and dump truck loading on Showground Road. Measurement dominated by vehicles passing, bats in trees and crickets in the grassed area, as well as a train passing. |

NOTES

Monitoring results showed that actual noise impacts were below predicted levels for all occasions. Dominant noise sources included passing vehicles along Showground Road and Mann Street, fauna activity and nearby recreation activities (i.e. greyhound track races on the 7/10 and 28/10). The work activities were usually noted as a low hum during monitoring. No noise related complaints were received from any activities undertaken during the month. Affected sensitive receivers were notified of the upcoming works via letter box drops.

Dust Deposition Results

Air concentration limits are specified in EPL Condition L2.4.  Table 2 specifies the Air Concentration Limits for the Project.

Table 2 Air Concentration Limits

| Pollutant | Units of Measure | 100 percentile concentration limit | Reference Conditions | Oxygen correction | Averaging period |
| --- | --- | --- | --- | --- | --- |
| Insoluble solids | Grams per square metre per month | 4 | Maximum total insoluble solids |  | Month |

Details on the location of the three Dust Deposition Gauges are provided in Table 3 and in Figure 1. The monitoring locations are consistent with EPL Condition P1.1.

Table 3 Monitoring Locations

| EPA Identification no. | Type of Monitoring Point | Location Description |
| --- | --- | --- |
| 2 | Dust deposition gauge (reference gauge) | 73A Showground Road, Narara |
| 3 | Dust deposition gauge | 520 Pacific Highway, Wyoming (near crusher site) |
| 4 | Dust deposition gauge | 4 Renwick Street Wyoming (crusher site) |

Table 4 Monitoring Results

| Monitoring Point | Date | Units of Measure | Insoluble solids | 100 percentile concentration limit |
| --- | --- | --- | --- | --- |
| October 2014 |
| EPA 2 | 15/09/14 – 15/10/14 | Grams per square metre per month | 1.4 | 4 |
| EPA 3 | 15/09/14 – 15/10/14 | Grams per square metre per month | 1.0 | 4 |
| EPA 4 | 15/09/14 – 15/10/14 | Grams per square metre per month | 1.6 | 4 |

Surface Water Discharge Monitoring

Licence condition L2.1 states that for each monitoring discharge point or utilisation area specified in the table below, the concentration of a pollutant discharged at that point, or applied to that area, must not exceed the concentration limits specified for that pollutant in the table Licence condition L2.5 details water concentration limits. These limits are detailed below in Table 4. The monitoring data results can be found in Table 5.

Table 4- Water concentration limits

| Pollutant | Units of Measure | 100 percentile concentration limit |
| --- | --- | --- |
| Oil and grease | Visible | Visible |
| pH | pH | 6.5 – 8.5 |
| Total Suspended Solids | Milligrams per litre (mg/L) | 50 |

Table 5- Surface water discharge monitoring results for October 2014

| EPA Monitoring Point | Location | Total Suspended Solids (mg/L) | Turbidity (NTU) | pH | Oil and Grease | Date of Release |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | Brady's Gully | 9.5 | 21.5 | 8.5 | Not visible | 2/10/2014 |
| 8 | Wyoming Creek | 30.4 | 36.6 | 8.26 | Not visible | 2/10/2014 |
| 5 | Lindsey St (E4) | 26.9 | 32.4 | 7.2 | Not visible | 16/10/2014 |
| 5 | Lindsey St (E4) | 8.4 | 10.1 | 7.9 | Not visible | 18/10/2014 |
| 1 | Brady's Gully | 10.2 | 23.2 | 8.5 | Not visible | 21/10/2014 |
| 1 | Brady's Gully | 10.2 | 23.2 | 7.9 | Not visible | 21/10/2014 |
| 8 | Wyoming Creek | 16.5 | 19.9 | 7.4 | Not visible | 24/10/2014 |
| 8 | Wyoming Creek | 18.8 | 22.6 | 7.9 | Not visible | 27/10/2014 |
| 8 | Wyoming Creek | 20.0 | 24.1 | 7.5 | Not visible | 28/10/2014 |
| 8 | Wyoming Creek | 20.6 | 24.8 | 7.9 | Not visible | 29/10/2014 |
| 8 | Wyoming Creek | 19.9 | 24 | 7.6 | Not visible | 30/10/2014 |
| 8 | Wyoming Creek | 20.5 | 24.7 | 8.1 | Not visible | 31/10/2014 |
| 8 | Wyoming Creek | 20.1 | 24.2 | 7.7 | Not visible | 1/11/2014 |