Gosford Passing Loops Monitoring Data

| Licensee: | Downer Edi Works Pty Ltd | Address: | 15 Watt St, Gosford | EPL No. | 20269 |
| --- | --- | --- | --- | --- | --- |
| Sampled: | Throughout May | Obtained: | Throughout May | Published: | 06/06/2014 |

|  | Noise Monitoring Results |
| --- | --- |
| Location | Date | Time | Measured (LAeq 15 min) | Predicted noise level | Comments |
| 77 Showground Road, Narara | 17/05/14 | 0521 | 59.6 | 57.6 | Construction of rail turnout. Rail saw operating 50 dB. Steady state dominated by traffic on Showground Road 69 – 72 dB. |
| 77 Showground Road, Narara | 17/05/14 | 0804 | 62.9 | 57.6 | Construction of rail turnout. 2 Dozers and 1 tracked loader operating 49 – 51 dB. Steady state dominated by traffic on Showground Road 69 – 72 dB. |
| 23 Racecourse Rd, Gosford | 17/05/14 | 0842 | 43.8 | 51.3 | Overhead wiring works involving 2 hi rail boom lifts and 1 scissor lift. Results dominated by Traffic on Showground Rd. |
| 31 Dwyer Street, North Gosford | 17/05/14 | 0902 | 57.6 | 87.1 | Excavation of ULX involving 5t excavator hammering. |
| 24 Campbell Street, Gosford | 17/05/14 | 0928 | 51.3 | 69.3 | Excavation of electrical trenches and ULX around the switchyard involving the vacuum truck and 8t excavator. |
| 30 Akora Road, Wyoming | 17/05/14 | 0951 | 44.5 | 52.8 | Installation of inter track drainage on the down involving an 8t excavator and bobcat. |
| 77 Showground Road, Narara | 17/05/14 | 1315 | 62.9 | 57.6 | Construction of rail turnout. 8t excavator and 1 tracked loader operating 45 dB. Steady state dominated by traffic on Showground Road 67 – 69 dB. |
| 23 Racecourse Rd, Gosford | 17/05/14 | 1337 | 44.6 | 51.3 | Overhead wiring works involving 2 hi rail boom lifts and 1 scissor lift. Results dominated by Traffic on Showground Rd. |
| 31 Dwyer Street, North Gosford | 17/05/14 | 1359 | 58.4 | 87.1 | Excavation of ULX involving 5t excavator hammering. |
| 24 Campbell Street, Gosford | 17/05/14 | 1424 | 52.5 | 69.3 | Excavation of electrical trenches and ULX around the switchyard involving the vacuum truck and 8t excavator. |
| 16 Campbell Street, Gosford | 17/05/14 | 1441 | 49.8 | 88.5 | Excavation of ULX involving 8t excavator hammering. |
| 12 Akora Road, Wyoming | 17/05/14 | 0951 | 54.5 | 58.8 | Installation of inter track drainage on the down involving an 8t excavator and bobcat. |
| 23 Racecourse Rd, Gosford | 17/05/14 | 2242 | 40.1 | 51.3 | Overhead wiring works involving 2 hi rail boom lifts and 1 scissor lift. Results dominated by Traffic on Showground Rd. |
| 77 Showground Road, Narara | 18/05/14 | 0028 | 54.1 | 57.6 | Construction of rail turnout. 8t excavator and 1 front tipper operating 46dB. Steady state dominated by traffic on Showground Road 67 – 69 dB. |
| 24 Campbell Street, Gosford | 18/05/14 | 0056 | 49.7 | 63.5 | Excavation of electrical trenches and ULX around the switchyard involving a bobcat and 8t excavator. |
| 5 Cary Street, Wyoming | 18/05/14 | 0117 | 45.2 | 53.7 | Excavation of ULX involving 8t excavator and front tip truck |
| 77 Showground Road, Narara | 18/05/14 | 0302 | 48.3 | 57.6 | Construction of rail turnout. 8t excavator and 1 front tipper operating 55dB. Steady state influenced by traffic on Showground Road 67 – 69 dB. |
| 24 Campbell Street, Gosford | 18/05/14 | 0522 | 48.3 | 63.5 | Excavation of electrical trenches and ULX around the switchyard involving a bobcat and 8t excavator. |
| 23 Racecourse Rd, Gosford | 18/05/14 | 0809 | 41.5 | 51.3 | Overhead wiring works involving 2 hi rail boom lifts and 1 scissor lift. Results dominated by Traffic on Showground Rd. |
| 31 Dwyer Street, North Gosford | 18/05/14 | 0844 | 49.2 | 87.1 | Excavation and backfilling of ULX involving 5t excavator hammering. |
| 16 Campbell Street, Gosford | 18/05/14 | 0908 | 49.4 | 88.5 | Excavation and backfilling of ULX involving 5t excavator hammering. |
| 24 Campbell Street, Gosford | 18/05/14 | 0926 | 54.3 | 69.3 | Excavation of electrical trenches and ULX around the switchyard involving the vacuum truck and 8t excavator. |
| 10 Akora Road, Wyoming | 18/05/14 | 1016 | 54.5 | 58.8 | Installation of inter track drainage on the down involving an 8t excavator and bobcat. |
| 77 Showground Road, Narara | 18/05/14 | 1051 | 63.7 | 57.6 | Construction of rail turnout. 8t excavator and 1 front tipper operating 47dB. Steady state influenced by traffic on Showground Road 67 – 69 dB. |

NOTES

Monitoring results showed that actual noise impacts were below predicted levels. Three exccedances were recorded at 77 Showground Road due to the high level of non-construction related noise at receiver (frequent vehicle pass by on Showground Rd). Observations during the measurement showed construction impacts were below the levels predicted in the NVIS. Affected sensitive receivers were notified of the upcoming works via letter box drops and where required were offered respite in accordance with the projects Noise and Vibration Management Plan and the Community Liaison Plan. Monitoring for the Overhead Wiring Works was done at 30m and a calculated impact produced due to high level of non-construction related noise at receiver.

Dust Deposition Results

Air concentration limits are specified in EPL Condition L2.4.  Table 2 specifies the Air Concentration Limits for the Project.

Table 2 Air Concentration Limits

| Pollutant | Units of Measure | 100 percentile concentration limit | Reference Conditions | Oxygen correction | Averaging period |
| --- | --- | --- | --- | --- | --- |
| Insoluble solids | Grams per square metre per month | 4 | Maximum total insoluble solids |  | Month |

Details on the location of the three Dust Deposition Gauges are provided in Table 3 and in Figure 1. The monitoring locations are consistent with EPL Condition P1.1.

Table 3 Monitoring Locations

| EPA Identification no. | Type of Monitoring Point | Location Description |
| --- | --- | --- |
| 2 | Dust deposition gauge (reference gauge) | 73A Showground Road, Narara |
| 3 | Dust deposition gauge | 520 Pacific Highway, Wyoming (near crusher site) |
| 4 | Dust deposition gauge | 4 Renwick Street Wyoming (crusher site) |

Table 4 Monitoring Results

| Monitoring Point | Date | Units of Measure | Insoluble solids | 100 percentile concentration limit |
| --- | --- | --- | --- | --- |
| May 2014 |
| EPA 2 | 14/4/14 – 13/5/14 | Grams per square metre per month | 1.1 | 4 |
| EPA 3 | 14/4/14 – 13/5/14 | Grams per square metre per month | 1.2 | 4 |
| EPA 4 | 14/4/14 – 13/5/14 | Grams per square metre per month | 0.6 | 4 |

Surface Water Discharge Monitoring

Licence condition L2.1 states that for each monitoring discharge point or utilisation area specified in the table below, the concentration of a pollutant discharged at that point, or applied to that area, must not exceed the concentration limits specified for that pollutant in the table Licence condition L2.5 details water concentration limits. These limits are detailed below in Table 4. The monitoring data results can be found in Table 5.

Table 4- Water concentration limits

| Pollutant | Units of Measure | 100 percentile concentration limit |
| --- | --- | --- |
| Oil and grease | Visible | Visible |
| pH | pH | 6.5 – 8.5 |
| Total Suspended Solids | Milligrams per litre (mg/L) | 50 |

Table 5- Surface water discharge monitoring results for May 2014

| EPA Monitoring Point | Location | Total Suspended Solids (mg/L) | Turbidity (NTU) | pH | Oil and Grease | Date of Release |
| --- | --- | --- | --- | --- | --- | --- |
| 6 | Dwyer St (E5) | 7.9 | 7.9 | 8.4 | Not visible | 1/05/2014 |
| 1 | Brady's Gully | 13.4 | 13.4 | 8.4 | Not visible | 5/05/2014 |
| 1 | Brady's Gully | 13.2 | 13.2 | 7.2 | Not visible | 6/05/2014 |
| 6 | Dwyer St (E5) | 33.8 | 33.8 | 7.2 | Not visible | 7/05/2014 |
| 1 | Brady's Gully | 28.5 | 28.5 | 7.8 | Not visible | 7/05/2014 |
| 6 | Dwyer St (E5) | 12.4 | 12.4 | 8.02 | Not visible | 12/05/2014 |
| 1 | Brady's Gully | 40 | 40 | 7.8 | Not visible | 12/05/2014 |
| 6 | Dwyer St (E5) | 43.2 | 43.2 | 8.4 | Not visible | 14/05/2014 |
| 1 | Brady's Gully | 10.8 | 24.6 | 7.8 | Not visible | 14/05/2014 |
| 1 | Brady's Gully | 19.1 | 43.4 | 8.3 | Not visible | 15/05/2014 |
| 1 | Brady's Gully | 10.6 | 24.1 | 8.1 | Not visible | 16/05/2014 |
| 1 | Brady's Gully | 10.7 | 24.3 | 8.3 | Not visible | 19/05/2014 |
| 6 | Dwyer St (E5) | 14.9 | 14.9 | 7.9 | Not visible | 20/05/2014 |
| 1 | Brady's Gully | 22.5 | 51.1 | 7.8 | Not visible | 20/05/2014 |
| 6 | Dwyer St (E5) | 9.4 | 9.4 | 8.47 | Not visible | 26/05/2014 |
| 6 | Dwyer St (E5) | 3.1 | 3.1 | 8.35 | Not visible | 27/05/2014 |
| 6 | Dwyer St (E5) | 10.9 | 10.9 | 6.9 | Not visible | 30/05/2014 |